## Slide 1
Process Problem
3
Downstream FIC-08 recorded NO VALUE
2
Only 2-3% of total liquid sent is collected (after 21 h)
1
Pump is working as expected
4
No pressure build-up observed
5
LIC takes long time to respond after complete draining
6
LIC took 4 h to open (at 5 ml / h)
Observations
60% mass balance closure,
5-6 h run, low liquid collection,
negligible gas
- Ambient,
- 5 ml/h,
- isoprene only
Test
Condition
isoprene vapor pressure: 0.724 atm absolute @ RT
0.32 atm at 5oC
ASSUMPTIONS
Liquid
pump
flash vessel
FIC
PCV
Process
vent
GC
Local
vent
Chilled
@5oC
Liq. collection
Blower suction applied
Isoprene (Boiling Point 34oC) will flash-boil violently when transferred from the cold separator into the warm collection vessel.
draining vessel is connected to a local vent with suction. This means the pressure inside the collection vessel is likely below atmospheric pressure (a partial vacuum). Lower pressure drastically lowers the boiling point of the isoprene, causing even faster vaporization and loss directly to the vent as saturated vapour
Liquid flow is steady
No hold up
two-phase flow (vapor + entrained liquid droplets) is incompatible with most common thermal MFCs
interpret the unstable/very low flow as an error or an out-of-range measurement, forcing the reading to zero
?
?
low liquid density (0.68 g/ml) and high vapor volume
contradicting
The initial 5 \ml flow rate must first saturate the 10 ml hold-up volume with this vapor before any steady-state condensation can occur.
the low liquid density and high vapor volume, consumes a significant amount of the initial liquid feed before the condensation rate can truly start exceeding the vaporization rate. The 5oC in the separator is enough to condense some vapor, but not enough to completely suppress vaporization.
a large amount of the incoming liquid immediately flashes/vaporizes upon entering the lower-pressure, warmer section of the separator before reaching the coldest condensing surface.
Pump has a 25-psi check valve
7
no leak
No obvious loss
Thermal MFCs work on heat capacity principle
Complete draining disturbs the stable mass balance between the input flow, the accumulation threshold, and the dominant vapor loss
Validation