## Slide 1
1
Fewer Skids, Broader Remit, Faster MOC Cadence
Why Now?
Lab consolidation
Fewer capability units in service, each carrying a broader remit than before
The same skid now serves ad hoc requests across very different chemistries, not one fixed process
Every new chemistry or envelope change on a shared capability triggers its own management-of-change cycle
Manual hazard-basis prep can't keep pace with an ad hoc, high-frequency request cadence
The result: safety review volume and frequency are rising faster than headcount can absorb them — the same shared capability now needs an SafetyLens basis prepared far more often than the old
3
2
Capability-based model
4
Review bottleneck
Frequent MOCs

## Slide 2
Every run ends at a named human sign-off. The tool drafts the basis; it never accepts the risk.
1
What It Is — And Why the Draft Can Be Trusted
Disagreement is preserved
Four independent analytical passes run on the same evidence. Conflicts between them are shown to the workshop, never quietly averaged away.
A synthesis and calculation-screening agent, not a decision-maker. From a short input form and connected SOPs, P&IDs, prior HAZID/HAZOP, RHAs, design data and literature, it produces an evidence-classified E-HAZID draft — hazard identification only. It never runs HAZOP worksheets, LOPA, safeguard or ESD assessment, and it never approves an operation.
3
2
4
Every finding is tiered
Evidenced, Inferred, or Gap — shown explicitly, never blended into one confident narrative tone.
It never invents site data
Public constants (LFL/UFL, exposure limits, API 941, NIST) are cited and used; missing site-specific data is labeled a gap, not filled in.
It has no approval authority
The operating reality this tool is built for — not a hypothetical efficiency case

## Slide 3
Design Principle I — Manufacturing Disagreement
Retrieval alone can't replicate a room of people who disagree — so disagreement is engineered directly into the method via four independent passes over the same evidence
Pass 1
Documentation-Trusting
Assumes SOPs, P&IDs and design data are accurate and current. Builds the hazard picture straight from what's written — the baseline reading.
Pass 2
Skeptic & Deviation
Explicitly assumes the as-built unit has drifted from the documents. Asks what modification, bypass, or undocumented change would make Pass 1 wrong — forces reasoning about staleness rather than treating text as ground truth.
Pass 3
Operator's-Eye
Reasons from a field/operations perspective: manual interventions, sampling habits, nuisance conditions that get worked around — what a design document structurally cannot capture.
Pass 4
Cross-Discipline Interaction
Hunts for hazards at the boundary between disciplines — a metallurgy issue that only matters because of an instrumentation blind spot, a process change that invalidates a mechanical assumption.
Reconciliation, not resolution: conflicts between passes are shown explicitly — “Pass 1 assumed X; Pass 2 flags that X may not hold because Y” — never quietly averaged into one confident narrative. Disagreement is a feature of the output, not noise to smooth away.

## Slide 4
Design Principle II — Evidence Integrity & the Human Handoff
A confidently wrong number is worse than no number — so every claim is routed, tagged, and eventually handed to a named accountable reviewer
1
Calculation integrity
Every quantitative claim routes through actual tools — NIST/DIPPR data, a reactivity database such as NOAA/EPA's CRW, or a process simulator — never free-text model arithmetic. What can't be verified is flagged, not guessed.
2
Three-tier evidence tags
Every finding is marked Evidenced (cites document/page), Inferred (general literature), or Gap (no data — flag for SME). The tiers are never blended into one uniformly confident tone.
3
Document silence is a finding
If a known hazard class is plausible but never mentioned in site documents, that silence is flagged explicitly as a possible gap — not read as confirmation the hazard is absent.
4
Analogous-incident weighting
Literature and incident search explicitly targets structurally similar units (same reaction class, same catalyst family), tagged “analogous, not site-specific” so reviewers treat it as a prompt, not a confirmed site risk.
5
Judgment forks stay with humans
Credibility-of-deviation calls and other ambiguous, judgment-heavy points are presented as explicit forks for the review team — the agent never resolves them on its own.
6
Tiered document gating
Tier 1 evidence (P&IDs, SOPs, design limits, SDSs) missing hard-stops or heavily caveats the run. Tier 2/3 absence is logged as a gap, never silently skipped.
Positioning: a rigorously sourced draft that seeds a human HAZID workshop — never “the report”, to avoid institutionalizing whatever gaps exist in the document set. “Unresolved / Requires Human Judgment” and the Evidence Gaps Register are structurally load-bearing sections, not appendices, and a qualified reviewer signs off before anything is final.